## Slide 1: Modeling of pintle-type injector internal fuel flow and in-cylinder spray behavior of SA HCCI z-engine
Victor Akimov, Andrey Kuleshov
Bauman Moscow State Technical University

## Slide 2
SA HCCI realization in Z-engine
Due to specific in-cylinder temperature behaviour; massive internal EGR; fuel injection (by pintle-type injector) into a gas having low density the SA HCCI is possible!
Injection with pintle-type injector into a burnt gas when exhaust is near to terminating and intake has not started yet:
71 deg. before TDC. - p = 2,5 bar; T = 800 K; EGR=100%.
Injection pressure up to 1100 bar. SMD ~ 10 mm
Notes: Эти доработки сделать для презентации ДИЗЕЛЬ-РК в части PCCI для Пежо

## Slide 3: Simulation of in-cylinder spray behavior
Ansys Fluent discrete phase model
(Euler-Lagrangian approach)

## Slide 4: Experimental validation of non-evaporating injection
Experiment condition (Andreas Schmid et.al.) | 
Ambient gas density, kg/m³ | 2,2; 6,6
Ambient gas | Air (300K)
Fuel | Isooctane (300K)
Fuel density | 732,1
Injection pressure drop, Mpa | 12
Spray cone angle, deg | 90
6.6kg/m³ , 750 ms after SOI
6.6kg/m³, 350 ms after SOI
2.2kg/m³,
450 ms after SOI
Andreas Schmid experiment
Chart: Time, ms
| 0 | 5.0000000000000017E-2 | 0.1 | 0.15000000000000005 | 0.2 | 0.25 | 0.3000000000000001 | 0.35000000000000009 | 0.45 | 0.55000000000000004 | 0.70000000000000018
This study 6.6kg/m³ | 0 | 6.33 | 10.8 | 13.9 | 16.1 | 18 | 19.4 | 20.6 | 22.7 | 24.4 | 26.5
Experiment 6.6kg/m³ | 0 | 4 | 8 | 12 | 15 | 17.5 | 20 | 22 | 24 | 26 | 28
This study 2.2kg/m³ | 0 | 7.5 | 13.7 | 19.1 | 23.6 | 27.6 | 30.8 | 33.3 | 37.4
Experiment 2.2kg/m³ | 0 | 5 | 10 | 15 | 20 | 24 | 28 | 31 | 35.5 | 39 | 43

## Slide 5: 2D vs 3D
Experimental
shadowgraphy of similar injector
in similar condition
3D case visualization
2D case visualization
Chart: Time, ms
| 0 | 9.0000000000000028E-3 | 1.7999999999999999E-2 | 2.700000000000001E-2 | 3.7999999999999999E-2 | 4.5999999999999999E-2 | 4.9000000000000016E-2 | 5.3999999999999999E-2 | 6.7000000000000004E-2
3D case | 0 | 2.5 | 3.9 | 5 | 6.7 | 8 | 8.4 | 9.1 | 11.1
2D case | 0 | 1.74 | 3.53 | 5.63 | 7.7 | 9.8
Chart: Time, ms
| 0 | 9.0000000000000028E-3 | 1.7999999999999999E-2 | 2.700000000000001E-2 | 3.7999999999999999E-2 | 4.5999999999999999E-2 | 4.9000000000000016E-2 | 5.3999999999999999E-2 | 6.7000000000000004E-2
3D case | 70 | 65.2 | 60 | 52.4 | 38.6 | 31 | 27 | 22 | 14.3
2D case | 70 | 62 | 52 | 34.4 | 22.6 | 16.7
Definition | Computing time of 7,5 CAD injection duration, hours
2D | 12
3D | 110

## Slide 6: Comparison of results of single droplet heating and evaporation obtained by different methods
Experiment condition (Sazhin et.al.) | 
Ambient gas | Air
Ambient pressure, MPa | 3
Ambient temperature, K | 880
Injected droplet material | n-dodecane
Injected droplet initial temperature, K | 300
Injected droplet initial diameter, mm | 20
Injection velocity, m/s | 1
Fluent Convection/Diffusion controlled model (Miller, Sazhin)
Chart: Time, ms
| 0 | 4.5
Vaporization temperature | 547 | 547
This study | 300 | 476 | 559 | 577 | 589 | 598 | 603 | 606 | 610
Sazhin experiment | 300 | 440 | 515 | 545 | 550 | 551 | 552 | 552 | 552 | 552
 | 0
 | 0
 | 0
Chart: Time, ms
| 0 | 0.6000000000000002 | 1.2 | 1.6 | 1.9000000000000001 | 2.27
Sreznevsky equation | 20 | 17.16 | 13.75 | 10.89 | 8.113 | 0
This study | 20 | 20 | 19.8 | 18.5 | 17.1 | 15.5 | 13.5 | 11.4 | 8.55 | 0
Sazhin experiment | 20 | 20.8 | 21 | 19.7 | 18 | 16 | 14 | 11 | 7 | 0
Model | 
Evaporation model | Diffusion controlled Convection/ Diffusion controlled (Miller, Sazhin)
Adjusted parameters | Tvap=560K (empirical equation)
Sreznevsky equation:

## Slide 7: Comparison of results of single droplet heating and evaporation obtained by different models
Very close results obtained by Sazhin experiment, by Sreznevsky law and in this study
It is necessary carefully adjust parameters of model
Real z-engine condition | 
Ambient gas | Air
Ambient pressure, MPa | 0.32
Ambient temperature, K | 748
Injected droplet material | Diesel fuel
Injected droplet initial temperature, K | 380
Injected droplet initial diameter, mm | 10,4
Injection velocity, m/s | 30
Model | 
Evaporation model | Diffusion controlled Convection/ Diffusion controlled
Adjusted parameters | Tvap=490K (Vyrubov)
Chart: Time, ms
| 0 | 0.1 | 0.3000000000000001 | 0.6000000000000002 | 0.8500000000000002 | 0.98899999999999999
Sreznevsky equation | 10.4 | 9.86 | 8.679 | 6.518 | 3.887 | 0
This study | 10.4 | 10.4 | 10.4 | 10.2 | 9.86 | 8.97 | 8.2 | 7.45 | 6.67 | 5.82 | 4.83 | 3.59 | 1.5 | 0
Chart: Time, ms
| 0 | 1
Vaporization temperature | 490 | 490
This study | 380 | 478 | 492 | 489 | 487 | 488 | 491 | 492 | 493 | 493 | 493 | 493 | 493
Heating time | 0

## Slide 8
Two-stage simulation of injection
Boundary conditions
First part: internal flow
(Cavitation, Air entraining)
Second part: in-cylinder region
(Breakup, Evaporation)
First part model | 
Total number of cells | 250 000
Average element size | 4 μm
Computer cluster | 528 Cores X 2800GHz/ 1Tb RAM
Computing time | 24 Hours / 7,5 CAD injection duration/ 32 cores employed
Models | VOF model / Realizable k-e turbulence/ Schnerr-Sauer cavitation
Simulation with
moving pintle
Export data from interface to BC of second part
- Liquid
- Vapor
- Air
Pintle type injector
Pressure, Temperature,
Turbulence, Velocity,
Mass flow rate, Blobs size
Droplet diameter 100 μm
(blobs)
- Droplet diameter 30 μm
- Droplet diameter 0.5 μm
Second part model | 
Total number of cells | 20 000
Average element size | 0.3mm
Computer | Core I7-2700K@3.5GHZ
Computing time | 14 Hours / 7,5 CAD injection duration/ 4 cores employed
Models | Discrete phase/ Realizable k-e turbulence/ SSD breakup/ Convection-diffusion controlled evaporation

## Slide 9
Conclusions
Fuel wets cylinder liner at full load conditions
Target of future research is search for solutions to bound spray tip penetration
- Initial droplet diameter 80mm
- Droplet diameter 30mm
- Droplet diameter 0.1..10 mm
Second part model | 
Total number of cells | 20 000
Average element size | 0.3mm
Computer | Core I7-2700K@3.5GHZ
Computing time | 14 Hours / 7,5 CAD injection duration/ 4 cores employed
Models | Discrete phase/ Realizable k-e turbulence/ SSD breakup/ Convection-diffusion controlled evaporation
Adjusted parameters | Breakup time constant B=3 (handbook) Tvap= 501,4 (Vyrubov)
Two-stage simulation of injection
Second part: Simulation of in-cylinder
evaporating spray behavior

## Slide 10
- Droplet diameter 20mm
- Droplet diameter 10mm
- Droplet diameter 1 mm
Dpin=2,5mm, inject. pressure 350 bar,
duration 0,22ms, m_f=0,011, Ca=0,8
Dpin=2,5mm, inject. pressure 800 bar,
duration 0,22ms, m_f=0,015, Ca=0,8
Dpin=2,5mm, inject. pressure 800 bar,
duration 0,22ms, m_f=0,011, Ca=0,5
Dpin=2,5mm, inject. pressure 800 bar,
duration 0,32ms, m_f=0,023, Ca=0,5
Search for solutions to bound spray tip penetration

## Slide 11: Multi-stage injection strategy
- 20mm
- 10mm
- 1 mm
Droplet diameter
- 0.3
- 0.2
- 0
Mass fraction of vapor
- 800K
- 600K
- 500К
Gas temperature
Conclusions
For HCCI operation in z-engine preferable:
from 3 to 4 stage of injections on regime of
maximum load
downsized injector geometry providing high
operation speed, high-pressure injection with
maximum area contraction (supercavitation regime
or closely to supercavitation)
earlier start of first injection (90 CAD before TDC)
lower design cone angle of pintle (about 90 deg)